## Slide 1: C. Computer Vision Algorithm
The robotic arm is programmed to move towards the position of a specific colored object
The color detection algorithm is written in Python using the OpenCV library
The vision sensor captures the real time video of the robotic arm and the object
The video is extracted frame by frame and each of the frame is processed through a series of steps to detect colored objects in the frame
Each frame is converted from BGR (Blue Green Red) image to HSV (Hue, Saturation and Value) image
A specific color is filtered by applying a lower and upper limit threshold to the HSV image

## Slide 2
The experiment is performed with blue color chosen as the object of interest.
The resulting image is eroded to remove the noise present in the image and dilated to fill the gaps in the image.
The threshold image is scanned to check the presence of contours. In case a contour is located the position of the contour is found by calculating moments
A minimum enclosing circle is drawn around the object and the center of the circle corresponds to the X and Y coordinates of the position of the object
The color detection algorithm is extended to capture data from two vision sensors and combined with the robotic arm control code to perform the desired task.

## Slide 3: III. EXPERIMENT AND RESULTS
The robotic arm is operated in the Cartesian mode
Initially the two vision sensors start capturing the video in real time.
A frame is extracted from the video captured by the vision sensor 1 and the X and Y position of the object is calculated using the color detection algorithm.
Before proceeding with the arm control, a condition is checked to see if the position of the object is same as or very close to its previous position (X ± 5). If the condition is true, it means the object has not moved and hence the arm remains in the base position. If it is false, it indicates that the object has been moved to a different location and the arm is controlled to move towards the new location of the object.
This way it eliminates the possibility of the arm to move to the same position repeatedly even if multiple frames are captured by the vision sensors.
If an object is detected by the vision sensor, the arm is moved to the base position (an inverted L) and the gripper is opened.
The arm is then moved up or down depending on the value of the Y coordinate with the threshold measured at 300.

## Slide 4
Arm Link software provided by Trossen Robotics is a simple graphic user interface (GUI) to control the InterbotiX line of robot arms
X coordinate range of the arm varies from 212 to 812 and can be controlled manually using the Arm Link software.
The pixel distance in the horizontal axis varies between 0 and 640 and is measured using the color detection algorithm.
The object is placed at different positions in front of the arm and multiple readings of the X distance in pixels and the corresponding X coordinate of the arm are taken and plotted in the Desmos graphing calculator.
A best fit equation of a line is formulated.
The factors 0.95 and 150 are calculated using trial and error method such that the line generated passes through a maximum number of points plotted.
X position of the arm = (X object * 0.95) + 150

## Slide 5
The arm is then controlled to move in the left or right direction depending on the value obtained from the equation
Now the robotic arm is moved to a position which is very close to the location of the target object.
There is a possibility that the obtained location might not be the exact location of the object. Hence the vision sensor 2 is used to obtain the accurate location of the object.
The X value in pixel is checked to see if it lies in the center of the frame. In the event it does not fall within the specified range,
the arm is moved in small steps in the left or right direction until
it reaches the center position. If the X value is already in the
specified range, no command is given to the arm.

## Slide 6: VII. CONCLUSION
Computer vision algorithm based on color detection has been developed to automate the movement of the robotic arm.
This was implemented by using two vision sensors to accurately find the location of the target object:
  First sensor was used for obtaining the coarse location of the object
  second one was used for fine localization.
The robotic arm has the ability to pick up objects placed at different locations on the upper and lower level with a success rate of 83.33%.
The main goal of performing the action of picking up the object under one minute is achieved

## Slide 7: VIII. FUTURE WORK
Future works aimed is implementing:
The wireless protocol: Operator at one end can control the robotic arm wirelessly at the other end.
Voice recognition to control a robotic arm or vision sensor over voice.
And the most advanced to make it mind-controlled robotic arm by connecting to existing neurons or to electrodes implanted into the human brain to decode the signals from the brain and use them to control a robotic arm
Depth sensors can be used in addition to vision sensors to increase the performance of the robotic arm control in order to minimize the number of unsuccessful attempts
Advanced vision algorithms can be used for pose estimation and size detection to detect same object at different angles